## Slide 1: GPU Architecture
Amod Malviya
Notes: Mindset
  Reasoning >> Facts
  We need to think aloud, not a test
  We’ll practice engineering intuition a lot
  Don’t trust everything I say

## Slide 2
High Level Overview
Break (10 mins)
Hardware Deep Dive
Break (10 mins)
Memory & Performance

## Slide 3
High Level Overview

## Slide 4: Basics
Amdahl’s Law
Everything has a latency
Throughput hides latency (when correctly used)

## Slide 5
CPU
GPU
x16 lanes
PCIe 4.0: 16Gbps/lane
100+ns
Memory
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
What kinds of talk?
Initialization
Memory alloc/dealloc
Data Transfer
Execute Code
A simplified model
of GPU
Nature of CPU – GPU talk?
async !
PCI Express
Notes: Device vs Host timeline
Demo: CPU vs GPU – which is faster? Multiply with min parallelisation

## Slide 6: High level program flow
Initialise
Allocate memory on GPU & copy data
Set up compute pipelines (specify flow of kernels/shaders)
Submit the pipeline for execution on GPU
Wait for completion
Read data from GPU
Free all resources

## Slide 7
GPU
CPU
SQ
CQ
In case of WebGPU?
Notes: Q: Any idea about how CPU – GPU talk most of the time? System calls?
The kernel itself is also communicated via SQ/CQ

## Slide 8: Initialization
File: vec-multiply.html
The main reference through which we interact with the GPU

## Slide 9: GPU Memory Allocation & Data Copy
File: vec-multiply.html
Allocate memory on GPU
Size of memory
Purpose
CPU  GPU data copy
Notes: Other kinds of buffers – UBO, Vertex etc.

## Slide 10: Compute Kernels The “logic” in GPU

## Slide 11
Threads
Work Items
Invocations
…
Thread block Workgroup
0
1
2
3
…
Grid
Notes: Each thread is executing exactly the same code (but with awareness of itself)
Q: Why do we need to group threads?

## Slide 12
start_index
width
Unit of work
Kernel / Shader
width
input array
our position in the grid topology
WGSL
why do we need this condition?
A kernel needs to infer its target work section from its topology
Array scalar multiplication
Notes: WGSL: Rust-y syntax
Q: How does it get compiled to GPU’s machine code?

## Slide 13
Memory
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
What if there’s not enough capacity for all the threads in a workgroup?
Warp / Wavefronts
Scheduler
Register Files
n-lane SIMD
n-lane SIMD
n-lane SIMD
Memory Cache
Notes: Explain: why we need the "if" condition from before
Each block is guaranteed to execute on the same ”core”, but can be split into multiple warps
Explain: context switching between warps
Explain: prior reservation of resources
There _has_ to be a limit on maximum thread groups
And a limit on max threads per group

## Slide 14: GPU code – kernels need context

## Slide 15: GPU code – get cranking!
GPU  GPU
data transfer
Execute ‘n’
workgroups of the kernel
Data context for
kernel

## Slide 16: Data Transfer: GPU  CPU
File: vec-multiply.html
Notes: Q: Why does CPU -> GPU copy have a dedicated method, while GPU -> CPU does not?
Assignment: Why GPU memory needs to be mapped before copy to CPU?

## Slide 17: WebGPU Shader Flow
HLSL
Direct3D
MSL
Metal
SPIR-V
Vulkan
Browser
WGSL
Compiler
Microsoft
Apple
Others

## Slide 18: Matrix Multiplication?
X
=
Notes: Q: How should we think about grid topology here?

## Slide 19: Break

## Slide 20
Hardware Deep Dive

## Slide 21: Multiplying an array
imul %ebx, %edx, %eax
…
…
…
…
23
%ebx
%edx
%eax
x
=
%eip
CPU core
Machine Code
ALU (INT EU)
The true “compute” provider
SISD
Notes: Demo: doubling array size doubles CPU time, but not GPU time (Amdahl’s Law in case of GPU)

## Slide 22: SIMD
ZMM0 – 512-bit register
64x 8-bit numbers
32x 16-bit numbers
16x 32-bit numbers
ZMM1 – 512-bit register
x
_mm512_mul_epu32 ( __mm512i array1, __mm512i array2)
=
ZMM2 – 512-bit register
16x 32-bit multiplications!
filled with ”23”
Still on CPU
Requires more EUs
ALU (INT EU)
Notes: History on x86: MMX -> SSE (1/2/3/4) -> AVX (1/2/512)
Limitations – less flexible, control flow missing, exposes width

## Slide 23: CPU vs GPU
PCIe
CPU core
Control
ALU
ALU
ALU
ALU
ALU
ALU
CPU core
Control
ALU
ALU
ALU
ALU
ALU
ALU
PCIe
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Control
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Control
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Control
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
ALU
Control
GPU Global Memory
Memory
Is it really so simple? What are the tradeoffs?
Notes: Latency vs throughput oriented design
Q: How good are CPUs in latency?
Demo: min parallelization
Q: Cost of high memory bandwidth in GPUs? Higher cost of manufacturing.

## Slide 24: SIMT
if (…)
else
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
…
…
…
…
…
// end if
…
Divergent Control Flow
An executing thread group will block on
longest thread (e.g. for loop)
if/else are executed serially
(in the same executing thread group)
Registers 









Notes: Demo: Heavy workload demo
Once started, cannot stop
Q: Does the “if” boundary condition from before lead to control divergence?
Assignment: Reflect on how SIMD is different from SIMT. Both seem to be doing the same job, isn’t it?

## Slide 25
INT32 cores
FP32 cores
Matrix cores
Scheduler
Register Files
m-lane SIMD
n-lane SIMD
x-lane SIMD
Memory Cache
Notes: Q: Why would we want to have different number of lanes?
Q: Can different cores be active at the same time?
Q: What’s the typical size of memory cache?
Q: Why is it so small?
Q: Why do we split up blocks into warps?

## Slide 26: Hardware - NVIDIA

## Slide 27
NVIDIA H100 Architecture
Notes: 4x 16-lane SIMD for INT32

## Slide 29: Hardware - AMD

## Slide 30
AMD CDNA3 whitepaper

## Slide 31: Hardware - Intel

## Slide 32
https://www.intel.com/content/www/us/en/content-details/824434/2024-intel-tech-tour-xe2-and-lunar-lake-s-gpu.html
Notes: Each Xe core:
  8x 512b vector engine
  8x 2048b XMX engine
  192KB Shared L1 / SLM

## Slide 33
https://www.intel.com/content/www/us/en/content-details/824434/2024-intel-tech-tour-xe2-and-lunar-lake-s-gpu.html
Notes: XMX: Xe Matrix eXtensions

## Slide 34
https://www.intel.com/content/www/us/en/content-details/824434/2024-intel-tech-tour-xe2-and-lunar-lake-s-gpu.html

## Slide 35
https://www.intel.com/content/www/us/en/content-details/824434/2024-intel-tech-tour-xe2-and-lunar-lake-s-gpu.html
Notes: Intel Lunar Lake will be using 2x of these, so 8 Xe2 cores + 8 RT units

## Slide 36: Apple – GPU vs Neural Engine
Source: https://apple.fandom.com/wiki/Neural_Engine
Tensor core type stuff
INT8, INT16, FP16
CoreML
Shader cores, RT cores
Metal / MPS
Usual CPU
Std languages/runtime
Notes: Why – more efficient (specialized) than GPU, and leaves GPU free for graphcis
No public info – assumed to have INT8, INT16 and FP16 support
Most NPUs are designed for inference, not training.

## Slide 37: Break

## Slide 38
Memory & Performance

## Slide 39
X
=
What’s the ops/B ?
A
B
C
Notes: 2 OP to 8 bytes per cell of A & B

## Slide 40
Computational Intensity (OPS/B)
Computational Throughput (GOPS)
Roofline Model
Max Bandwidth (GB/s)
Max Throughput (GOPS)
T3
T1
T2
Notes: Q: Do you see now why GPU memory bandwidths are so important?

## Slide 41
Scheduler
Register Files
m-lane SIMD
n-lane SIMD
x-lane SIMD
L1 + Local
Scheduler
Register Files
m-lane SIMD
n-lane SIMD
x-lane SIMD
L1 + Local
L2 Cache
Global Memory
(VRAM)
Capacitive Memory
(Large + Slow)
SRAM
(Small + Fast)
Notes: Q: Why is capacitive memory slow, while SRAM fast?
Q: Memory bandwidth of H100?

## Slide 42
https://chipsandcheese.com/2024/06/25/testing-amds-giant-mi300x/

## Slide 43
https://chipsandcheese.com/2024/06/25/testing-amds-giant-mi300x/

## Slide 44
https://chipsandcheese.com/2024/06/25/testing-amds-giant-mi300x/

## Slide 45
https://chipsandcheese.com/2024/06/25/testing-amds-giant-mi300x/

## Slide 46
https://chipsandcheese.com/2024/06/25/testing-amds-giant-mi300x/

## Slide 47
X
=
A
B
C
Can we do better?
Caching?
Notes: Q: Do we see the advantage of spatial locality in a threadgroup now?
Q: What about B-transpose?

## Slide 48
X
=
A
B
C
Tiling
A1
A2
A3
A4
B1
B2
B3
B4
C1
C2
C3
C4
Notes: Assignment: implement tiling

## Slide 49: Optimisations
Maximising occupancy
Coalesced access for global memory
Minimising control divergence
Tiling of reused data
Privatisation
Thread coarsening
Programming Massively Parallel Processors – Hwu, Kirk, Hajj

## Slide 50: Thank you
Notes: Congratulations: now you know more about GPUs than 99% of BLR’s software engineers!
Assignment: (Puzzle) Idx-Add-Mul vs Num-Add-Mul – CPU vs GPU. Explain.