## Slide 1: Boundary Conditions
Reviewing Mental Models of Hardware & Software
Amod Malviya
Notes: QR code: https://github.com/amodm/talks/discussions/1

## Slide 2: Preamble
We use code to study CPU architecture
Code deliberately designed to amplify specific behaviours
“Reasoning “ >> “knowing facts”
Participation is mandatory
Designed to provoke study of CPU Arch, not a substitute for it
Hardware dependent results (but trends should be same)
Compiler: clang -O2 -g -fno-slp-vectorize
Notes: Goal is to show that hardware has real world implications on software
Peak performance can be achieved only if we understand how things work

## Slide 3: Amdahl’s Law
Performance improvement is dominated by
the slowest poke

## Slide 4: Stack vs Heap
sum_array(heap_arr, n)
sum_array(stack_arr, n)
?
~=
Notes: Which is faster?
Or does it depend on `n`?
Incorrect model: stack is “closer”, heap is “farther”
Correct model: subject to same caching pattern, all memory addresses are the same distance away.
Source: stack-heap.c

## Slide 5
heap
stack

## Slide 6: CPU Backend

## Slide 7
How much time should this take per iteration? (assume large count)
Consecutive: 1.3ns/iter
Random: 126 ns/iter
~100x difference ??
Notes: Source: memory-access.c
How much time per iteration? Depends? On what?

## Slide 8
CPU
Memory Bus
Memory is SLOOOOWWWWWW
Latency: 50-100 ns
Bandwidth: 25-50 GB/s /channel

## Slide 9
Memory Controller
L3
L1
Register File
L2
L1
Register File
Core 0
Core 1
Register
1 cycle
> 1 TB/s
L1
5 cycles
1 TB/s
L2
15 cycles
1 TB/s
L3
75 cycles
500 GB/s
DRAM
50ns
25 GB/s
CPU
Memory Hierarchy
Notes: The “cycles” here are CPU clock cycles
Note that while DRAM latency is ~50ns, actual latency would be L3 latency + DRAM latency.

## Slide 10
CPU
Memory Bus
Memory is SLOOOOWWWWWW
Latency: 50-100 ns
Bandwidth: 25-50 GB/s /channel
req1
50ns
8 bytes
req2
50ns
8 bytes
100ns: 16 bytes
= 160 MB/s
??
Burst!
req1
50ns
8 bytes (x8) = 64 bytes
Throughput hides latency by ammortising cost!
BL8
Notes: Link between BL and cache line size
Channel count increase is another example of using throughput to hide latency

## Slide 11
Cache Configuration
macOS (M1 Max)
Linux (x64)
Notes: Notice the differing caches in perf vs efficiency cores of M1
Notice the Instruction vs Data cache segregation for L1

## Slide 12
Exact same execution speed?
Faster by 10-50 %
Notes: Source: superscalar.c
x1-x7 are random numbers initialized at runtime.

## Slide 13
Frontend
Execution
Memory
Instruction Fetch & Decode
Reorder Buffer
Scheduler
L3
L1 Data
L2
L1 Instruction
ALU
ALU
ALU / VEC
LDST
AGU
LDST
….
High level
CPU Architecture
μops

## Slide 14
Credit: https://en.wikipedia.org/wiki/Instruction_pipelining

## Slide 15: CPU Frontend

## Slide 16
Consistent execution speed?
Notes: Source: bp.c
Is it existence of a condition that creates a problem?

## Slide 17
Frontend
Execution
Memory
Instruction Decoder
Reorder Buffer
Scheduler
L3
L1 Data
L2
L1 Instruction
ALU
ALU
ALU / VEC
LDST
AGU
LDST
….
μops
Fetch Queue
Branch Predictor
Notes: If there’s a branch predictor keeping track of taken branches, can we create a test to overflow its state?

## Slide 18
CPU Frontend is limited by control flow
CPU Backend is limited by memory access

## Slide 19: CPU vs GPU
Notes: Source: cpu-vs-gpu.html at https://github.com/amodm/talks/tree/main/lecture-series-hwsw/lecture-2-inside-the-gpu
Show single core comparison
Show multiple core comparison
Show divergent control flow
CPUs are optimized for latency, while GPUs are optimized for throughput oriented workloads

## Slide 20: CPU vs GPU
PCIe
CPU core
Control
EU
EU
EU
EU
EU
EU
CPU core
Control
EU
EU
EU
EU
EU
EU
PCIe
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
Control
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
Control
GPU Global Memory
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
Control
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
Control

## Slide 21: SIMT
if (…)
else
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
…
…
…
…
…
// end if
…
Divergent Control Flow
An executing thread group will block on
longest thread (e.g. for loop)
if/else are executed serially
(in the same executing thread group)
Registers 









Notes: Demo: Heavy workload demo
Once started, cannot stop
GPUs aren’t good at divergent control flow situations

## Slide 22: Books
Computer Architecture – Hennessy & Patterson
Programming Massively Parallel Processors, 4th ed – Hwu & Kirk

## Slide 23: Questions?
Notes: QR code: https://github.com/amodm/talks/discussions/1
Why did we not discuss I/O ?

## Slide 24
CPU
Memory Bus
RAS (Activate Row)
CAS (Activate Col)
Command: Read
Row Activated
tRP
tRCD
Col Activated
Send Data
CL
DDR4-3200 is 3200 MT/s, means 1600MHz clock, means 0.625ns clock.
Timing of 32-32-32 (CL-tRCD-tRP) means CL = tRCD = tRP = 32 cycles = 20ns
Memory is SLOOOOWWWWWW

## Slide 25: Advanced
Notes: SIMD
Memory Alignment
TLB flush
Cache associativity
Cache coherency as a distributed systems problem